## Slide 1: Design Space Exploration of FPGA - based CNN
Presentation By : Under The Guidance Of :
Vibha Pant Dr. Madhura Purnaprajna
BL.EN.P2EBS15022
M.Tech : Embedded Systems
Amrita School Of Engineering

## Slide 2: Contents
Motivation
Introduction
Abstract
Convolution Neural Networks
Literature Survey
TileNet: Proposed Architecture
Estimation Model
Estimation Results
Conclusion
References

## Slide 3: Motivation
Advanced Driver Assistance Systems(e.g. TI SoC - TDA3x[13])
  Affordable, high performance and low power
Self Driving Cars(Nvidia Drive PX [14])
  Map raw pixels to steering commands
                [ref Google]
Notes:   Combining deep learning, sensor fusion and surround vision

## Slide 4: Introduction
Artificial Neural Networks
Notes: Artificial Neural Networks
  Composed of multiple nodes imitate the biological neuron
  Nodes take in inputs , perform simple functions on the data and return activation value, nodes connected by weight
Fc each neuron connected to all neurons of the the previous layer so we have a lot of weights

## Slide 5: Convolutional Neural Networks
CNN Layers:
  Convolution : Computationally Intensive
  Pooling
  ReLu:f(x) = max(0,x)
  Fully Connected : Memory Intensive
Ref[12]
ANN
CNN

## Slide 6: Convolution Layer: Algorithm
Ref[4]: Pseudo code Convolution Layer
IFM 8 Bit array of N*R*Col Dimension*
OFM 8 Bit Array of M*R*Col Dimension
Kernel 2 Bit Array of M*N*K*K Dimension
Input Feature Map(IFM)
Output Feature Map(OFM)
Kernel(Weights)
R
Col
N
M
N
K
K
R
Col
M
*Assuming S=1, Padding of (K-1)/2 to ensure output dimensions are same as the input dimensions

## Slide 7: Deep CNN: AlexNet

## Slide 8: AlexNet
Layer | Input Depth(N) | RinxCin | Output Depth(M) | RoutxCout | Weight Vector
Conv1 | 3 | 227x227 | 96 | 55x55 | 11x11
Pool1 | 96 | 55x55 | 96 | 27x27 | 3x3
Conv2 | 48 | 27x27 | 256 | 27x27 | 5x5
Pool2 | 256 | 27x27 | 256 | 13x13 | 3x3
Conv3 | 256 | 13x13 | 384 | 13x13 | 3x3
Conv4 | 192 | 13x13 | 384 | 13x13 | 3x3
Conv5 | 192 | 13x13 | 256 | 13x13 | 3x3
Pool 5 | 256 | 13x13 | 256 | 6x6 | 3x3
FC6 | 9216 | 1x1 | 4096 | 1x1 | -
FC7 | 4096 | 1x1 | 4096 | 1x1 | -
FC8 | 4096 | 1x1 | 1000 | 1x1 | -

## Slide 9
                EXISTING WORK

## Slide 10: Computational Optimization
  Network Binarization:
    Deterministic Binarization using sign function or clipping
    Weights /and activation functions
    Eg. Binary Connect[7]
  Network Ternarization:
    Ternarization of weights using optimal thresholds
    32 bit weights to be replaced by 2-bit ternary weights(-1,0,1)
    Multiply-Accumulate as Multiplexer, two’s complement and adders(eliminate multiplication in inference) [1]
  Compressing pre-trained deep networks:
    Pruning redundant, non-informative weights in a previously trained network reduces the size of the network at inference time [4]

## Slide 11: Binary Vs Ternary NN
CNN | Weight | Activation | Scheme | Accuracy(MNIST)
Binary Connect[7] | -1,1 | Full Precision | Deterministic Binarization | 98.82%
Ternary WN[1] | -1,0,1 | Full Precision | Optimization with threshold-based Ternarization function | 99.35%
Planned Ternary Weight Network | -1,0,1 | 8 bit | Optimization with threshold-based Ternarization function | To be Analyzed

## Slide 12: Existing Work: CNN on FPGA
 | Technique | Performance |  | Platform
FINN, Feb 2017[3] | Weights and Activation function are binarized |  | MNIST | Zynq , Xilinx.
 |  | Accuracy | 95.8% | 
 |  | Latency | 12.3M/ 0.31 us | 
 |  | Power | 11.3W | 
 |  | GOPS | 11600 | 
Ternary Neural Networks for Resource-Efficient AI Applications[2] | Weights and Inputs are ternarized | Accuracy | 96.58 | Kintex 7, Xilinx
 |  | Latency | 195K images/s20.5us | 
 |  | Power | 3.8W | 
 |  | GOPS | Not Reported | 
Notes: FINN binary ip and wts , sigmoid
Ternary uses student teacher approach, thershold

## Slide 13: Existing Work: Ternary CNN on FPGA
Nurvitadhi et al Ref[19]
Ternary Scheme for weights
32 bit floating point Adders
Approx. 60% better than Titan X
Best case performance is still limited to 16 TOPS

## Slide 14: Abstract
TileNet: a novel tiled architecture for CNNs with ternarized weights achieving high throughput (30-40 TOPs) and high accuracy.
Notes: fpga as cortex of brain general purpose, highly parallel
reconfig,prototyping for using fpga
Conv higher parallel degree and more reources
In FC reduce the mem bandwidth
Performance analysis
Cnn accelerator: reduce memory space vs explore parallelism
We cant store all the weights on chip as well
Data reuse/ data precision reduction
Parallelism: inter op, intra op, parallelism within cnv
Optimizaton of mem badwicth and computuin

## Slide 15: Challenges
High throughput(10’s of TOPS)
High Accuracy
Large Data Sets (ImageNet)

## Slide 16: Proposed Architecture
  TileNet
  Generic tiled architecture
  Ternary CNNs
  Independent of the network architecture
  High Throughput 30-40 TOPS
  High Accuracy

## Slide 17: TileNet: Architecture
  Compute Tile
  Memory
    RSB
    Weight Memory
    Intermediate Memory

## Slide 18: Ternary Multiplier
  Weights as +1,0,-1
  Multiplier replaced by Mux Logic
Weight Vector | Output
"00" | 0
"01" | Input
"10" | 0
"11" | 2's compl (Input)

## Slide 19: Compute Tile

## Slide 20: Parallelization of Compute
Parallelization Factor “C”

## Slide 21: Memory Organization

## Slide 22: Memory Organization

## Slide 23: Control FSM for Layeri
Wt_c: count for parallelization factor C
Int_Mem: Intermediate Memory
Cols: Columns written into Int_Mem
Nxt_l: indicate when next layer can begin

## Slide 24: Streaming Architecture

## Slide 25: Systolic Architecture

## Slide 26: ESTIMATION MODEL

## Slide 27: Estimation Model
Based on constraints and architecture
  Throughput
  Memory Utilization
  Area Utilization
Determine Parallelization

## Slide 28
                ESTIMATION RESULTS

## Slide 29: Compute Estimation :AlexNet
Device | xc7vx1140(Virtex 7)
LUTS | 712000
FFS | 1424000
BRAMS | 1880
Layer | N | M | K | N_T | Rin | Cin | Rout | Cout | C | M/C value | Max Pooling | Ternary Compute | LUTS
Conv1 | 3 | 96 | 11x11 | 16 | 224 | 224 | 55 | 55 | 16 | 6 | 3x3 | 2592 | 50688
Conv2 | 48 | 256 | 5x5 | 4 | 55 | 55 | 27 | 27 | 128 | 2 | 3X3 | 3456 | 67584
Conv3 | 256 | 384 | 3x3 | 1 | 13 | 13 | 13 | 13 | 64 | 6 | NA | 13824 | 270336
Conv4 | 192 | 384 | 3x3 | 1 | 13 | 13 | 13 | 13 | 64 | 6 | NA | 10368 | 202752
Conv5 | 192 | 256 | 3x3 | 1 | 13 | 13 | 13 | 13 | 64 | 4 | 3X3 | 6912 | 135168
Total |  |  |  |  |  |  |  |  |  |  |  | 37152 | 726528
%LUTS | 102.04
Freq | 500MHz
Throughput | 37.15 TOPS
Time to complete(ms) | 0.101024
Throughput = Total ternary compute*2*Frequency
Parameters:
N - Depth of Input feature Map
M - Depth of Output feature Map
k - Weight Vector width
N_T - No. of tiles in Weight Vector
Rin,Cin - IFM width and height
Rout,Cout - OFM width and height
C - Parallelization factor
M/C - No. of pixels computed in parallel

## Slide 30: Memory Estimation :AlexNet
Layer | N | M | K | Input Memory(BRAMS) | Kernel Memory(BRAMS) | Total | % Utilization
Conv1 | 3 | 96 | 11x11 | 6 | 72 | 78 | 4.14893617
Conv2 | 48 | 256 | 5x5 | 36 | 96 | 132 | 7.021276596
Conv3 | 256 | 384 | 3x3 | 96 | 284 | 380 | 20.21276596
Conv4 | 192 | 384 | 3x3 | 72 | 288 | 360 | 19.14893617
Conv5 | 192 | 256 | 3x3 | 72 | 192 | 264 | 14.04255319
 |  |  |  |  |  | 1214 | 64.57446809

## Slide 31: Estimation vs Implemented Results
Chart: Estimated LUT vs Reported LUT (%)
| C1 | C2 | C3 | C4 | C5
ESTIMATED% LUT | 7.1191 | 9.4921 | 37.9685 | 28.4764 | 18.9843
REPORTED % Impl LUT | 5.0581 | 7.3338 | 27.1 | 20.36 | 14.36
Chart: Estimated BRAM vs Reported BRAM(%)
| C1 | C2 | C3 | C4 | C5
Estimated Memory BRAM Util % | 4.1489 | 7.0213 | 25.5319 | 19.1489 | 14.0426
Reported Memory % | 4.1 | 7 | 20.2 | 19.1 | 14

## Slide 32: Compute Estimation : AlexNet Systolic
Layer | N | M | K | N_T | Rin | Cin | Rout | Cout | C | M/C value | Max Pooling | Ternary Compute | LUTS
Conv1 | 3 | 96 | 11x11 | 16 | 224 | 224 | 55 | 55 | 2 | 48 | 3x3 | 20736 | 405504
Conv2 | 48 | 256 | 5x5 | 4 | 55 | 55 | 27 | 27 | 16 | 16 | 3X3 | 27648 | 540672
Conv3 | 256 | 384 | 3x3 | 1 | 13 | 13 | 13 | 13 | 24 | 16 | NA | 36864 | 720896
Conv4 | 192 | 384 | 3x3 | 1 | 13 | 13 | 13 | 13 | 24 | 16 | NA | 27648 | 540672
Conv5 | 192 | 256 | 3x3 | 1 | 13 | 13 | 13 | 13 | 16 | 16 | 3X3 | 27648 | 540672
Total |  |  |  |  |  |  |  |  |  |  |  | 36864 | 720896
Device | xc7vx1140(Vertex 7)
LUTS | 712000
FFS | 1424000
BRAMS | 1880
%LUTS | 101.02
Freq | 500MHz
Throughput | 36.864 TOPS
Time to complete(ms) | 0.315648

## Slide 33: AlexNet: Across Devices
Chart: AlexNet : TOPS Variation Across Devices
| Virtex | Kintex | Artix | Zync
TOPs | 37.152 | 16.272 | 7.056 | 14.976
Chart: Resource Utilization
| Virtex | Kintex | Artix | Zync
%lut-l util | 102.0404 | 106.5666 | 102.5141 | 105.5746
%lut-m util | 69.8936 | 76.8586 | 140.8219 | 91.5894
Resource | Virtex | Kintex | Atrix | Zync
#Logic slices | 178000 | 74650 | 33650 | 69350
#BRAMS(36 kb) | 1880 | 955 | 365 | 755

## Slide 34: Across Networks
Chart: Throughput Across Networks
| LeNet | AlexNet | ResNet-50 | VGG
TOPs | 33.8688 | 37.152 | 17.082 | 25.659
Chart: Utilization Across Networks
| LeNet | AlexNet | ResNet-50 | VGG
%lut-l util | 93.0229 | 102.0404 | 46.9169 | 70.4742
%lut-m util | 56.7149 | 69.8936 | 99.2553 | 93.5239

## Slide 35: Conclusion
High parallelism in FPGAs achieves TOPS required
Generic TileNet Architecture Scaling
  Across Network
  Devices
  Across Systolic and Streaming architecture

## Slide 36: References
Li, Fengfu, Bo Zhang, and Bin Liu. "Ternary weight networks." arXiv preprint arXiv:1605.04711 (2016).
H. Alemdar, N. Caldwell, V. Leroy, A. Prost-Boucle, and F. P´etrot. Ternary Neural Networks for Resource-Eﬃcient AI Applications. CoRR, abs/1609.00222, 2016
Yaman Umuroglu, Nicholas J. Fraser, Giulio Gambardella, Michaela Blott, Philip Leong, Magnus Jahre, Kees Vissers ,FINN: A Framework for Fast, Scalable Binarized Neural Network Inference, CoRR, 2017
Gysel, Philipp. "Ristretto: Hardware-oriented approximation of convolutional neural networks." arXiv preprint arXiv:1605.06402 (2016).
Rahman, Atul, Jongeun Lee, and Kiyoung Choi. "Efficient FPGA acceleration of Convolutional Neural Networks using logical-3D compute array." Design, Automation & Test in Europe Conference & Exhibition (DATE), 2016. IEEE, 2016.

## Slide 37: References
Courbariaux, Matthieu, Bengio, Yoshua, and David, Jean-Pierre. Training deep neural networks with low precision multiplications. ArXiv e-prints, abs/1412.7024, December 2014.
Courbariaux, Matthieu, Bengio, Yoshua, and David, Jean-Pierre. Binaryconnect: Training deep neural networks with binary weights during propagations. ArXiv e-prints, abs/1511.00363, November 2015.
Courbariaux, M., Bengio, Y.: Binarynet: Training deep neural networks with weights and activations constrained to +1 or -1. CoRR (2016)
Gupta, S., Agrawal, A., Gopalakrishnan, K., and Narayanan, P. Deep Learning with Limited Numerical Precision. In Proceedings of the 32nd International Conference on Machine Learning (ICML-15), pp. 1737–1746, 2015.
Gysel, P., Motamedi, M., and Ghiasi, S. Hardware oriented approximation of convolutional neural networks. arXiv:1604.03168, 2016.
Rastegari, V. Ordonez, J. Redmon, and A. Farhadi, “XNORNet: ImageNet classification using binary convolutional neural networks,” CoRR, vol. abs/1603.05279, 2016.

## Slide 38: References
cs231n.github.io/convolutional-networks/
Prashanth Viswanath ,Mihir Mody, Mathew Manu et all,” A Diverse Low Cost High Performance Platform for Advanced Driver Assistance System (ADAS) Applications”, Texas Instruments
www.nvidia.come/object/drive-px.html
ImageNet Classiﬁcation with Deep Convolutional Neural Networks, Alex Krizhevsky, Ilya Sutskever, Geoffrey E. Hinton
DNPU: An 8.1TOPS/W Reconfigurable CNN-RNN Processor for General-Purpose Deep Neural Networks, Dongjoo Shin, Jinmook Lee, Jinsu Lee, Hoi-Jun Yoo, ISSCC 2017 / SESSION 14 / DEEP-LEARNING PROCESSORS / 14.2
Li, Huimin, et al. "A high performance FPGA-based accelerator for large-scale convolutional neural networks." Field Programmable Logic and Applications (FPL), 2016 26th International Conference on. IEEE, 2016.
Nurvitadhiet.al, 2017). Can fpgas beat gpus in accelerating next-generation deep neural networks? In Proceedings of the 2017 ACM/SIGDA International Symposium on Field-Programmable Gate Arrays , FPGA ’17, pages 5–14, New York, NY, USA. ACM
Simonyan, K. and Zisserman, A. (2014). Very deep convolutional networks for large-scale image recognition. CoRR, abs/1409.1556.

## Slide 39
                Thank You!